1) Flash memory extraction

1.1) Determine flash memory location

What is the address of the beginning of the flash memory segment?
0x08000000
What is the size of the flash memory segment?
0x00200000

2) Find the open TCP port

Which TCP port number is open?
4242

3) Find the relevant part of the firmware

3.1) Find incoming data storage location

Address and size of data SRAM region
address: 0x20000000
size: 0x00030000

Command to dump SRAM contents
dump_image sram_dump 0x20000000 0x00030000

How I located my input in the memory dump
Used proposed command: grep -b -o -a 'austin' sram_dump

Byte address that input is found at
0x2001 0D54 was the most consistent address that part of the string would be stored at

68948 (byte offset so divide by 4 for word offset): (5 times) (only has the first 4 bytes)
0x10D54 → 0x2001 0D54

Watchpoint triggers
1) PC = 0x080015e8
2) PC = 0x08005f10

What is the address of this load instruction, and what is the starting address of the function that it is a part of?

Load instruction address: 0x08005f0e
Function address: 0x08005ee0

4) Protocol Determination

General Protocol Format

Field Bits	Description	Requirements	Field Size (bytes)
[0:3]	← “SPKR”	String	4
[4:7]	← Don’t Care Field? (any 4 byte value?)	4
[8:11]	← Message Length	(value <= 0x8001)	4
[12]	← Speaker Cmd	(0 < value < 7 )	1
[13:?]	← Message?	? (varies?)

What are the sizes of the various fields in the command message?
Field Size Shown in table

What are any requirements on the values of certain fields for this command?
Requirements shown in table

Can you identify how the data from particular fields are used?
Shown in description mostly

What does each command do in the context of audio playback?
Speaker Cmd	Description
0 → init	(BLANK)
1 → play	(BLANK)
2 → add_samples	(BLANK)
3 → pause	(BLANK)
4 → unpause	(BLANK)
5 → stop	(BLANK)
6 → status	(BLANK)

What is the format of reply messages from the speaker?

What information is included in replies from the speaker?