1.) Binary water balloon general program information

• What is the target architecture of the binary?
ARM-32 bit
• Is the binary statically or dynamically linked?
Statically
• Are symbols stripped?
No, we can still see the names of library functions and don’t need to reverse engineer them to know what they mean.

Some strings I saw were interesting that referred to the startup message, as well as some other strings I haven’t seen yet.

• What is the register size of this architecture?
32 bit registers

• What is the endianness of this architecture?
Little Endian (Default) for this file

• How are arguments passed to functions?
Through registers r0,r1,r2,r3, and via the stack if there are more than 4 arguments.

• How is an integer return value from a function passed back to the calling function?
It is returned through r0 when 32 bits, but r1-r3 can optionally be used to extend the return	value size to 64bits-128bits.

2.) Binary Water Balloon Analysis

Phase_1
“Indiana, our Indiana” – Only string that passes Phase_1

Phase_2
“256 128 64 32 16 8” – Only string that passes Phase_2. Requires 6 arguments starting from	256, and halves itself each time.

Phase_3
“16 150”, “15 379”, “14 882”, “13 589”, “12 229”, “11 889”, “10 39” - 1st argument calculates the case statement to jump to, and 2nd argument is compared with a constant and if equal, returns.

Phase_4
“5 5”, “6 8”, “7 13”, “8 21”,”9 34”, “10 55” are possible answers

Function: Only accepts 5-10 inclusive as argument.
        Adds the return values of the 2 functions
        before it such that
fun(x) = fun(x-1) + fun(x-2)

to generate a pattern such as:

fun(5) = fun(4)+fun(3)=3+2 =5
fun(6) = fun(5)+fun(4)=5+3 =8
fun(7) = fun(6)+fun(5)=8+5 =13
fun(8) = fun(7)+fun(6)=13+8=21
fun(9) = fun(8)+fun(7)=21+13=34
fun(10)= fun(9)+fun(8)=34+21=55

Had to figure out fun(3), fun(4), fun(5) to
see this fibonacci pattern.

Phase_5
“0 966 99”, “1 405 988”, “2 906 0”, “3 803 346”, “4 41 395”, “5 462 829”, “6 178 653”, “7 840 87”

Starting at address 0x95098 lies some addressable data.
1st argument will determine at what offsets the data is read into the program. The first argument can be an unsigned number that is <=7.
2nd and 3rd argument should match the corresponding data read at those offsets.

Increasing the 1st argument by 1 will change the offset of the data read into the program by 8 where argument 3 is always 4 bytes ahead of argument 2 in the data table.

Phase_6
“8<:1305”, ”8<:13>5”, ”(,*!# %”, ”(,*!#.%”, “HLJAC@E”, “HLJACNE”,
        “X\ZQSPU”, “X\ZQS^U”, “hljac`e”, “hljacne”, “x|zqspu”, “x|zqs~u”

Any input with an ascii string like x8 xC xA x1 x3 (x0 or xE) x5 will index the string
"puamcheztqilrspv" to spell “triumph” where the x indicates a don’t care because the most signficiant half-byte is ignored. The least significant half byte of each character is what indexes the main string to spell triumph. ‘p’ repeats itself in the main string, so that is why we can use x0 or xE interchangeably to index ‘p.’

Secret Phase

Can be initiated with the input from phase 4 by providing 2 integers and a specific string “Rainbows”.
In phase_complete, upon having 6 correct inputs and 0 skips, a sscanf() checks address 0x96010 for these inputs. At this address, I noticed a value that was equivalent to my input from phase 4. All that was missing was the string, which can be added to trigger the secret phase.

Through dynamic analysis, __aeabi_idivmod(r0, r1) takes in 2 arguments. It doesn’t return anything, but it will store modulo of those two arguments in r1, and the lowest value of those two arguments will be stored in r0 eventually. Afterwards, fun(r0, r1) will be called and this cycle will continue UNTIL the remainder is 0 in r1. The value returned in r0 should be 6 for the program to pass.

Also, no matter what inputs you give the program such as “6 12” or “12 6”, the program will correct it so that the higher of the two values is stored in r0 and the lower is stored in r1 before __aeabi_idivmod is called. So, with either inputs above, r0 would store 12 and r1 would store 6 before entering the function.

An example of a working input and the process to break it down:

“12 6”
first stage: 12 mod 6 where the remainder 0 is stored in r1 and the lower of the two values, 6, is stored in r0. Since the remainder is 0, we will return r0 and it just so happens to be 6.

A more complicated example of a working input:

“18 60” (inputs are corrected)
first stage: 60 mod 18 where the remainder 6 is stored in r1 and the lower arg 18 is stored in r0
second stage: 18 mod 6 where the remainder 0 is stored in r1 and the lower arg 6 is stored in r0
Since the remainder is 0, we will return r0 and it just so happens to be 6.

Inputs appear to fit this process IF

1) Both inputs are divisible by 6
AND
2) The difference between the inputs is also 6
OR
3) The Modulo of the inputs is also 6.

I’m not sure if there are other conditions, but those are the conditions I noticed. Otherwise I would just follow the process above.

3.) Standard Library function identification

#1
• How many arguments does this function take?
3 (r0,r1,r2)
• What are the types of the arguments? (Pointer, integer, etc.)
r0,r1 – Pointer types r2 - Integer
• What is the type of the returned value?
Integer, specifically the difference between 2 bytes.
• Describe what the function does. If you recognize this standard library function, you
can simply list the name. If you do not, describe the functionality as best you can.

The function appears to be ‘int memcmp(const void *str1, const void *str2, size_t n)’

Takes two addresses through r0 and r1 and an integer through r2. Generally speaking, the function de-references r0 and r1, increments their addresses, and compares their two byte values by subtracting the value at r1 from the value at r0 (*r0 - *r1).

If the byte values are equal, it loops through this again, and checks if the index matches r2. If the Index matches r2, then 0 is returned. This index tells us how many bytes we have addressed and so it’s presumed that r2 is pre-set to the size of the address range to index.

If the byte values aren’t equal, then it returns the result from subtraction (*r0 - *r1).

This function seems to compare two strings in memory. If the strings are equal, then they will stop comparing as soon as the size set in r2 is reached.

If string 1 (r0) is larger then it will return a positive integer.

If string 2 (1) is larger then it will return a negative integer.

#2
• How many arguments does this function take?
3 (r0,r1,r2)
• What are the types of the arguments? (Pointer, integer, etc.)
r0, r1 – Pointer r2 - Integer
• What is the type of the returned value?
Pointer, r0 remains unchanged and is returned as the same value.
• Describe what the function does. If you recognize this standard library function, you
can simply list the name. If you do not, describe the functionality as best you can.

Appears to be ‘void *memcpy(void *dest, const void * src, size_t n)’

In short, storing values at *r0 from *r1, for r2 indices.
Take in 2 pointers through r0 and r1 and an integer through r2.
Copy r0 to r3 to preserve the starting address of r0 since it is also the return value.
Load bytes from r1 address and store at r3 address (and increment r3 address).
Check if the value copied is null and increment r1 address if it is not.
Compare our index value with r2 to check if we reached the size of bytes we are copying.
We return the original r0 address once this size is reached.